## Slide 1: Firefighter Indoor Navigation using Distributed SLAM (FINDS)
Major Qualifying Project
Matthew Zubiel
Nick Long
Advisers:
Prof. Duckworth, Prof. Cyganski

## Slide 2: Need for Firefighter Location
Worcester Cold Storage Fire, December 1999
  In total, 6 firefighters died after becoming lost
  Need for outside personnel to keep track of responders indoors
Incident Commanders need current location of each first responder
  Communicate directions to firefighters
  Direct rescue teams to downed firefighter
Photo Credit :Worcester Telegram and Gazette

## Slide 3: Technologies of Indoor Navigation and Tracking
GPS cannot be used indoors
Alternative ways to track:
  RF-Based Localization and Tracking
  Inertial Based Tracking
  Dead Reckoning
  Simultaneous Localization and Mapping (SLAM)
    Build a map of the environment with no prior knowledge of surroundings
    Build a track of the location of a user

## Slide 4: Simultaneous Localization and Mapping
EKFMonoSLAM [1]
Requires an image set for input
Detects features (corners) in images, and correlates detected corners from frame to frame
Produces predictions for both feature location and track
[1] Javier Civera, Oscar G. Grasa, Andrew J. Davison, J. M. M. Montiel, 1-Point RANSAC for EKF Filtering: Application to Real-Time Structure from Motion and Visual dometry, to appear in Journal of Field Robotics, October 2010.
Sample EKFMonoSLAM Output

## Slide 5: Our Approach
Initially attempted to develop a “real-time” tracking system
  Processing time was very long
We attempted to take responsibility off EKFMonoSLAM by implementing functionality remotely
Video capture and corner detection were moved to a mobile unit
  Mobile unit sent coordinates of detected corners to base station (laptop)
Photo Courtesy Popular Science
Mobile Unit
Base Station

## Slide 6: Project Goals
Capture and process images in real time
Send resulting data to base station
Develop method to provide EKFMonoSLAM algorithm with input
Configure EKFMonoSLAM algorithm to accurately track motion using corner-only input
Run 2 scenario based tests, and compare experimental results with expected results
  A. Straight Line Test
  B. 90-Degree Turn

## Slide 7: Mobile Unit Hardware Components
2 Components
  VmodCAM Stereo Camera Module
  Atlys FPGA

## Slide 8: Mobile Unit Implementation
3 HDL Components:
  1. Image Capture – Data from VmodCAM to rest of design
  2. Corner Detection Module – Detect corners in images from camera.
  3. Communications Module – Transmit corners to base station

## Slide 9: VmodCAM Module
Gather data from VmodCAM to the rest of design
  I2C Communication for RGB 565 color images
  Initial Testing using HDMI Display and DDR2 Memory from Digilent Provided Code
VmodCAM

## Slide 10: Corner Detection Approach
Harris Corner Detection Algorithm
  Corners found by determining a Harris value for every pixel
  Initial Simulations performed using MATLAB
Sample Harris Output using MATLAB

## Slide 11: VHDL Corner Detection Implementation
Pipelined Approach
  Operate on each pixel as it arrives

## Slide 12: VHDL Test Bench
Corner Detection Output
Simulated Input from Camera

## Slide 13: Ethernet Module
Utilizes Atlys Gigabit Ethernet capabilities and UDP protocol
Sends corners in the format:
  Valid, Y-Coordinate, X-Coordinate, Frame Number
  Sends 360 Corners at a time for data considerations

## Slide 14: Results: Corner Detection
Corner Detection Completed on Atlys FPGA
Original Image
FPGA Output

## Slide 15: Results: Corner Detection (cont)

## Slide 16: Complete System Testing
2 Scenario Tests Performed
  Straight Line and 90-Degree Turn

## Slide 17: Scenario Test – Straight Line

## Slide 18: Scenario Test – 90 Degree Turn

## Slide 19: Conclusions
Goal | Implementation
Capture and process images in real time | VModCAM Stereo Camera Module with FPGA Processing
Send resulting data to base station | Ethernet Module on FPGA with Base Station Receiver
Develop method to provide SLAM algorithm with input | Corner Detection on FPGA to base station receiver (black and white images)
Configure SLAM algorithm to accurately track motion using corner-only input | Modified settings in EKFMonoSLAM to reflect corner-only input
Run 2 scenario based tests, and compare experimental results with expected results | Video results
Successfully tracked the path of a person walking down a corridor

## Slide 20: Suggestions for Future Work
Before deployment, many improvements are required
  Power consumption must be analyzed for mobile power implementation
  Ethernet module must be replaced by wireless component
  Hardware must be ruggedized and form-factor must be minimized
  Base station (namely EKFMonoSLAM) needs to be optimized for real-time processing
Possible research into alternate SLAM algorithms
Additional, more comprehensive scenario testing
Thermal Camera Expansion